## Slide 1: Scaling the Pipeline
Stefan Boberg
Technical Director, Frostbite
@bionicbeagle
@FrostbiteEngine

## Slide 2: Frostbite Engine
Started 2004 as common DICE engine initiative
Now in general use within EA Games label
~15 titles in development
Diverse genres!

## Slide 3: Frostbite Engine – FPS

## Slide 4: Frostbite Engine – Racing

## Slide 5: Frostbite Engine – RPG

## Slide 6: Frostbite Engine – Action

## Slide 7: Frostbite Engine – RTS

## Slide 8: Scale / Dimensions
  Multi-site collaboration
    Shanghai, Europe, North America
  Large teams
    400+ contributors in some cases
  Multiple VCS branches
  Many target platforms
    PC, PS3, Xbox 360
  Content rich games

## Slide 9: Scale – Example (Battlefield 3)
Ballpark size
  500GB raw DCC assets
  80GB native Frostbite assets (’source data’), 100k files
  ~18GB target data (PC)
  100,000 individual build steps (PC)
Current games in development are larger
  Hello Bioware! 

## Slide 10: Frostbite Architecture
  Structured Storage
  Build-centric
  Single asset loading path
  Always preview on target
    Asset hotswap support
    Also, direct tweak path
  Some explicit live editing code in Game
  Let’s start looking at how the game handles assets and work our way ”backwards” through the pipe.
FrostEd
(.NET)
Celsius (asset db)
Blizzard (data build)
Avalanche (storage)
Game
Runtime

## Slide 11: Asset Packaging Model
Bundles
  Linear stream of assets (usually)
  Levels, sublevels (streaming)
Chunks
  Free streaming data blobs
  Texture mips, movies, meshes
Chunks are random access (pull)
Bundles are linear read only (push)
Superbundles are container files, storing bundles and chunks
  Data inside is visible once superbundle is mounted
.SB
Bundle
Bundle
Bundle
Bundle
Chunk
Chunk
Chunk
Chunk
Chunk
Chunk
Chunk
.SB
Chunk
Chunk
Chunk
Chunk
Chunk
Chunk
Chunk
Chunk
Chunk
Chunk
Chunk
Chunk
Chunk
Chunk
Chunk
Chunk
Chunk

## Slide 12: Packaging
During development, layout is stored in Avalanche Storage Service
  Stores full description of bundles and superbundles
  Stored as packages with chunk references
  Bundles are assembled on-the-fly when requested by game / tools (via HTTP)
  Game does not know the difference between network and disk builds (single path)
Complete packaging logic is executed every build pass
  Including iterative builds!
  So must be very fast

## Slide 13: Avalanche Storage Service
Core Frostbite component
Every developer runs an instance locally
Windows Service
  RESTful HTTP interface
  Via HTTP (server implemented using http.sys API)
    http.sys can serve data directly (in kernel mode) from system page cache (zero copy)
    Very scalable
  ... with significant optimizations for local access

## Slide 14: Avalanche Storage Service
Target (i.e built) data storage
Chunk store
Build results and build dependency tracking information
Layout information (defines packaging)
Network cache / build cache
Peer-to-peer build distribution
Message bus
Tracing/diagnostics infrastructure
Production metrics infrastructure
... and more

## Slide 15: Avalanche Storage Service – Chunk Store
“Branch” 1
  Content Addressable Storage
    Key-value storage (immutable)
    key = SHA1(value)
    Basic deduplication
    See: Venti, Git
  Other services rely on this heavily
    Build Store
    Build Cache
    Asset Database (Celsius)
  Base primitive: ”Package”
    JSON/BSON-like binary document format
    Usually with attachments (stored as chunk references)
Asset1
$.Asset1
Asset1’
Asset1
$.Asset1
Asset1’
Chunks
“Branch” 2

## Slide 16: Asset Pipeline Goals
  Time spent waiting for build = waste
  Optimize bootstrap time (initial build)
    Build throughput
  Optimize feedback time (iterative builds)
  Large games require extremely scalable solutions
  Challenging!
    And a bit of a thankless task… if people notice your work, it’s probably because you broke something, or it’s too slow! 

## Slide 17: Back of the envelope… bootstrap time
Building entire game from scratch
  Input: ~80 GB source data
  Output: ~18 GB target data
  Total: 100GB
If we would read and write all data at full speed
  Let’s say ~50MB/sec throughput
  100*1024/50 = 2048 sec = 34 minutes
  ... and that’s without any CPU work at all
  ... and with no additional I/O for temporary assets

## Slide 18: System Performance
CPU Performance
  Well understood
  Reasonable tools for analysis (Vtune, Very Sleepy, GlowCode, VS)
  Strings, strings, strings ....
Storage
  Not quite as well understood among game developers
  Often overlooked, often the bottleneck!
  Limited analysis tool knowledge
    ETW/Xperf (Windows Performance Toolkit)
    Resource Monitor, Performance Counters, code instrumentation

## Slide 19: Storage Hierarchy
 | Typical Latency | Typical Throughput
Registers | < 1nsec | n/a
Cache | < 10nsec | > 100G/sec
DRAM | < 500nsec | > 1G/sec
Network Cache | < 50 µsec | n/a
SSD | < 200 µsec | >200M/sec
HDD | < 20ms | >50M/sec

## Slide 20: Storage Hierarchy
It’s a CACHE HIERARCHY
  Larger caches help performance
  Free system RAM is used as cache
DON’T FORGET TO PUT A LOT OF MEMORY INTO WORKSTATIONS
  It will reduce the impact of I/O
  Working set fits in free RAM -> GOOD!
If the working set does not fit in system cache, performance falls off a cliff
  Just like CPU work when you don’t stay in L1/L2/L3 cache
We recommend our teams to get 32GB RAM workstations when purchasing
  They don’t!

## Slide 21: Storage
The fastest I/O request is the one you don’t!
Mission:
  Reduce seeks
  Reduce blocking on I/O

## Slide 22: Build Output - Avalanche
We don’t use traditional file system storage for storing build function outputs
We use packages and Log Structured Storage
Benefits:
  Single ’oplog’ file stores all build state (also used for dependency tracking)
  Mostly sequential I/O (attachments are stored in separate CAS pool)
  No fragmentation
  No file open/close overhead
  Cheap ’branching’
  Simple copying of build state from one machine to another – pick up where they left off
Asset1
Asset2
Asset3
Asset4
…

## Slide 23: Network Cache
Network is often faster than local storage
  Assuming data is in server RAM
  Remember the storage hierarchy!
  So ensure cache server has plenty of RAM
  Ideally the entire working set should fit in memory
  DICE server currently has 32GB RAM
    Should probably be upgraded
All nodes run an instance, and queries always go through the local instance
  Hierarchical
  Flexible topology (also: WAN replication for remote sites)

## Slide 24: Network Cache – Basic Cache
Uses key-value store over HTTP
Values are opaque blobs
Implemented in Avalanche Storage Service
  Using HTTP.SYS API – very efficient and scalable
  Leverages system cache for maximum throughput – no dedicated buffering
Data stored in Chunk Store
  Content Addressed Storage (CAS), SHA1 key
  Same content – same key => basic deduplication (”single instance storage”)
  As used by Git, Venti, etc
Metadata in Google LevelDB
Used for misc ad hoc caching (shaders, expensive computations)

## Slide 25: Network Cache – Package Cache
Structured values (”package”)
  Essentially, JSON documents (but in custom BSON-like binary format)
  Each package may have BLOB attachments
Used for data build caching
Same basic format used to persist ’normal’ build results
  Same data can be referenced from build results and cache package
  Zero copy
  Async fetch of bulk data not required for making build progress

## Slide 26: Build Caching Implementation
Keys generated from build inputs
  Input file contents (SHA1)
  Other state (build settings, etc)
  Build function version (’manual’ hash)
Cacheable build functions split into two phases
  First phase registers all the inputs
  Second phase does the work
Build scheduler
  Executes first phase
  Queries cache
  Use results if available – otherwise run second phase
Input A
Input B
Code
Cache Key

## Slide 27: Build Model
Apply function to map source data to target
  assettarget = f(assetsource, ...)
Goal: purely functional, no side effects!
  Easy parallelism
  Lazy Evaluation
Not quite there yet.
Requires some adjustment and initially more mental energy than the unfortunately very common basic ”blobby” and very stateful build structure.

## Slide 28: Benchmark – BF3 (PC)
Produces ~18GB build
  Time includes ”indexing” – i.e determining relationships between assets, metadata extraction, SHA1 hash for all files, pre-parsing XML files etc (@ 45s)
Best case build time - 15m30s (SSD, 2x Xeon 2687w, 32GB RAM)
  ~1GB/min
  Cached data already available locally
  CPU limited, not very parallel (avg 3 LP busy per target platform)
Clean system build time – 25 min
  Pulls down all data from network
  ~500MB/min
Room for improvement! (more async work, more parallelism)

## Slide 29: Asset Database (Celsius)
Data managed in Avalanche Storage Service
Similar implementation to build store
I.e Log Structured
Produced by a mapping process ”importing” data into the database
  Very much like the regular data build process!
  Data may be imported from native format files
  ... or other data sources (SQL, Excel, whatever)
Saving involves ”exporting” database assets back to files
  I.e a reverse mapping

## Slide 30: Celsius - Benefits
  No need to save to disk (or check out) before build
Snapshot isolation for builds
Cheap branching for creating multiple sessions
  I.e preview same level/object/shader side-by-side, different settings
Tightly integrated with build system
Fast sync
  Seconds to get up and running
  Lazy fetch
... tons more

## Slide 31: Q & A
Slides will be available shortly:
http://www.bionicbeagle.com
http://publications.dice.se